# C++ for Robotics

## Chapter 6: Micro Project
### Scene
This first part of the project will be based on an environment we've seen in this class, the Costa Coffee scenario:

### Rosbot
For this project, you will use the Rosbot robot:

### Task to accomplish
Create a C++ program that using the functions from the rosbot_class.cpp C++ file, helps the Rosbot get out of the cafeteria.
See in the first image where the robot starts, and where is the door at the top of it.
Just to help you out, let's make a summary of all the functions you've been using throughout the course:
- get_laser(index): As the name says, this function will allow you to get data from the laser of the robot. You will need to pass one parameter to this functions:
  - index: Here you need to specify a number between 0 and 719, which will indicate the direction of the laser reading.
get_laser_full(): As the name itself says, this function will allow you to get all the data from ALL the laser beams of the robot. As we've said before this is a total of 719 different readings. So, when called, this function will return a LIST containing all the 719 different readings from the laser beams.
- get_position(coordinate): This function returns the position of the robot in meters. You will need to pass one parameter to this function:
  - coordinate: Here you need to specify which coordinate you want this function to return: 1 for coordinate x, 2 for coordinate y, and 3 for coordinate z.
get_position_full(): This function will allow you to get the three coordinates of the position of the robot at that instant. This function will return a LIST containing the three coordinates: x,y,z, from the odometry of the robot.
- move_forward(seconds): This function allows you to move the robot in a straight line. You will need to pass one parameter to this functions:
  - seconds: Here you need to specify an integer number which will indicate for how many seconds will the robot move.
- turn(clock , seconds): As the name itself says, this function will allow you to turn the robot. You will need to pass two parameters to it:
  - clock: Specify here whether you want your robot to turn clockwise ("clockwise") or counter-clockwise ("counterclockwise").
  - seconds: Specify how long you want your robot to keep turning (in seconds).
stop_moving(): As the name says, this function will allow you to stop the robot from moving.
You can create a specific class for this exercise, as we did in exercise 6.1 and inherite the class of RosbotClass and all of its functions.
- Remember -
In order to be able to use the script, remember to run the program by doing:
In [ ]:
rosrun c_scripts unit6_exercise
Keep in mind that this exercise is a mix of exercises we've done in the previous chapters, and it could have many solutions. Please try to do it by yourself from start to finish, you will learn much more if you fight for each exercise, and the reward would be much bigger!
Try to be creative using the laser information, or the position information that the robot sensors provide us, and also drive the robot more intelligently by using for or while loops, and if else conditionals. See some examples:
- In the beginning we know that we have to turn right to get out of the kitchen before we reach the first wall. You can keep evaluating the distance given by the frontal value of the laser while you move. If that distance is too close (for example, closer than 2 meters) you can command the robot to start turning right.
- In the function turn you can only specify the direction of the turn and for how long (in seconds). Experiment with the number of seconds until you find how many are needed to turn 90 degrees.
- Going down the hall, the frontal value of the laser might not be very useful. You can also experiment with the position given by the function get_position, making the robot move until it has travelled a distance you decide (for example 8 meters). Remember to calculate distances between two different positions with the formula √(x1−x0)2+(y1−y0)2.
Include the package math.h to make use of the functions sqrt and pow if you need to.
Here you have the robot control class rosbot_class.cpp which you can directly call, or inherit in a new class, just as we did in example 5.1:
In [ ]:
#include "rosbot_control/rosbot_class.h"
#include "geometry_msgs/Twist.h"
#include "nav_msgs/Odometry.h"
#include "sensor_msgs/LaserScan.h"
#include "std_msgs/Float32.h"
#include "std_msgs/Int16.h"
#include "unistd.h"
#include <ros/ros.h>

#include <list>
#include <string>

using namespace std;

// RosbotClass constructor
RosbotClass::RosbotClass() {
  n = ros::NodeHandle("~");
  laser_topic = "/scan";
  laser_sub = n.subscribe(laser_topic, 10, &RosbotClass::laser_callback, this);
  vel_topic = "/cmd_vel";
  vel_pub = n.advertise<geometry_msgs::Twist>(n.resolveName(vel_topic), 1);
  odom_topic = "/odom";
  odom_sub = n.subscribe(odom_topic, 10, &RosbotClass::odom_callback, this);
  ROS_INFO("Initializing node .................................");
  usleep(2000000);
}

void RosbotClass::laser_callback(
    const sensor_msgs::LaserScan::ConstPtr &laser_msg) {
  laser_range = laser_msg->ranges;
  // ROS_INFO("Laser value: %f", laser_range);
}

void RosbotClass::odom_callback(const nav_msgs::Odometry::ConstPtr &odom_msg) {
  x_pos = odom_msg->pose.pose.position.x;
  y_pos = odom_msg->pose.pose.position.y;
  z_pos = odom_msg->pose.pose.position.z;
  // ROS_INFO_STREAM("Odometry: x=" << x_pos << " y=" << y_pos << " z=" <<
  // z_pos);
}

void RosbotClass::move() {
  // Rate of publishing
  ros::Rate rate(10);

  ros::Time start_time = ros::Time::now();
  ros::Duration timeout(2.0); // Timeout of 2 seconds
  while (ros::Time::now() - start_time < timeout) {
    ros::spinOnce();
    vel_msg.linear.x = +0.5;
    vel_msg.angular.z = 0.0;
    vel_pub.publish(vel_msg);
    rate.sleep();
  }
  vel_msg.linear.x = 0.0;
  vel_msg.angular.z = 0.0;
  vel_pub.publish(vel_msg);
}

void RosbotClass::move_forward(int time) {
  // Rate of publishing
  ros::Rate rate(10);

  ros::Time start_time = ros::Time::now();
  ros::Duration timeout(time);
  while (ros::Time::now() - start_time < timeout) {
    ROS_INFO_STREAM("Moving forward ........... ");
    ros::spinOnce();
    vel_msg.linear.x = 0.4;
    vel_msg.angular.z = 0.0;
    vel_pub.publish(vel_msg);
    rate.sleep();
  }
  vel_msg.linear.x = 0.0;
  vel_msg.angular.z = 0.0;
  vel_pub.publish(vel_msg);
}

void RosbotClass::move_backwards(int time) {
  // Rate of publishing
  ros::Rate rate(10);

  ros::Time start_time = ros::Time::now();
  ros::Duration timeout(time);
  while (ros::Time::now() - start_time < timeout) {
    ROS_INFO_STREAM("Moving backwards ........... ");
    ros::spinOnce();
    vel_msg.linear.x = 0.5;
    vel_msg.angular.z = 0.0;
    vel_pub.publish(vel_msg);
    rate.sleep();
  }
  vel_msg.linear.x = 0.0;
  vel_msg.angular.z = 0.0;
  vel_pub.publish(vel_msg);
}

void RosbotClass::turn(string clock, int n_secs) {
  ros::Rate rate(10);
  ros::Time start_time = ros::Time::now();
  ros::Duration timeout(n_secs);

  double WZ = 0.0;
  if (clock == "clockwise") {
    ROS_INFO_STREAM("Turning clockwise..............");
    WZ = -2.5;
  } else if (clock == "counterclockwise") {
    ROS_INFO_STREAM("Turning counterclockwiseeee ........... ");
    WZ = 2.5;
  }

  while (ros::Time::now() - start_time < timeout) {
    ros::spinOnce();
    vel_msg.linear.x = 0.5;
    vel_msg.angular.z = WZ;
    vel_pub.publish(vel_msg);
    rate.sleep();
  }
  vel_msg.linear.x = 0.0;
  vel_msg.angular.z = 0.0;
  vel_pub.publish(vel_msg);
}

void RosbotClass::stop_moving() {
  ROS_INFO_STREAM("Stopping the robot ........... ");
  vel_msg.linear.x = 0.0;
  vel_msg.angular.z = 0.0;
  vel_pub.publish(vel_msg);
}

float RosbotClass::get_position(int param) {
  if (param == 1) {
    return this->x_pos;
  } else if (param == 2) {
    return this->y_pos;
  } else if (param == 3) {
    return this->z_pos;
  }
  return 0;
}

list<float> RosbotClass::get_position_full() {
  list<float> coordinates({this->x_pos, this->y_pos, this->z_pos});
  return coordinates;
}

double RosbotClass::get_time() {
  double secs = ros::Time::now().toSec();
  return secs;
}

float RosbotClass::get_laser(int index) { return laser_range[index]; }

float *RosbotClass::get_laser_full() {
  float *laser_range_pointer = laser_range.data();
  return laser_range_pointer;
}

int main(int argc, char **argv) {
  ros::init(argc, argv, "rosbot_class_node");

  RosbotClass rosbot;

  rosbot.move();

  float coordinate = rosbot.get_position(1);

  ROS_INFO_STREAM(coordinate);

  return 0;
}
- Solution of the Mini Project -
unit6_exercise.cpp
In [ ]:
#include "rosbot_control/rosbot_class.h"
#include <ros/ros.h>

#include <math.h>
#include <string>

using namespace std;

class RosbotMove {
public:
  RosbotClass rosbot;
  void get_out();
  float calc_distance(float x0, float y0, float x1, float y1);
};

void RosbotMove::get_out() {
  rosbot.move_forward(1);
  while (rosbot.get_laser(0) > 1.75) {
    ROS_INFO_STREAM("Laser frontal reading: " << rosbot.get_laser(0));
    rosbot.move_forward(1);
  }
  rosbot.turn("clockwise", 3);
  rosbot.move_forward(2);
  rosbot.turn("counterclockwise", 3);

  // Get initial position
  float x_0 = rosbot.get_position(1);
  float y_0 = rosbot.get_position(2);
  float x_1 = x_0;
  float y_1 = y_0;
  float dist = calc_distance(x_0, y_0, x_1, y_1);
  while (dist < 8.00) {
    // Update current position
    x_1 = rosbot.get_position(1);
    y_1 = rosbot.get_position(2);
    dist = calc_distance(x_0, y_0, x_1, y_1);
    ROS_INFO_STREAM("Distance travelled: " << dist);
    // Keep moving
    rosbot.move_forward(1);
  }
  rosbot.turn("clockwise", 3);
  rosbot.move_forward(5);
  ROS_INFO_STREAM("Success!!!");
}

// function to calculate distance
float RosbotMove::calc_distance(float x0, float y0, float x1, float y1)
{
    // calculating distance
    return sqrt(pow(x1 - x0, 2) + pow(y1 - y0, 2));
}

int main(int argc, char **argv) {
  ros::init(argc, argv, "Rosbot_move_node");
  RosbotMove rosbot_moves;
  rosbot_moves.get_out();
}